## Slide 1
Bathymetry interpolation algorithms using AUV mission data
Alessia Annecchini
Alessia Guida
Lorenzo Irace
Giuseppe Longo

## Slide 2
Previously on this topic
Most performant algorithms
  Ideal case: spline interpolation
  Noise: kriging and spline interpolation
  Outliers: kriging and linear interpolation
    But kriging is slow...
Performances indexes: MSE and execution time (computing 95% confidence interval on 5 repetitions)
Seabed composition and water absorption
GUI setup

## Slide 3
Lineup
Outliers + noise
Mission physical bounds
Samples density

## Slide 4
Outliers + noise
Different magnitude
  Higher for outliers
Noise not filtered
  White Gaussian process
  Standard deviation
Random Gaussian seabed
Outliers rejection
  Matlab filloutliers method
  Not perfect

## Slide 5
Gaussian seabed: results
Algorithm |  | 
Linear | 1.9393 | 0.979798 ± 0.024702
RBF | 4.6236 | 37.460120 ± 3.960108
Spline | 2.3153 | 0.015477 ± 0.025418
Nearest neighbour | 4.7668 | 0.008748 ± 0.003283
Natural neighbour | 1.9393 | 1.178560 ± 0.143918
Biharmonic spline | 1.5180 | 24.704136 ± 7.127264
Minimum curvature | 1.5855 | 27.111282 ± 4.487095
Shepard (p = 4) | 2.2884 | 74.327256 ± 5.358215
Kriging | 1.2249 | 91.923460 ± 13.572509
Algorithm |  | 
Linear | 1.9393 | 0.979798 ± 0.024702
RBF | 4.6236 | 37.460120 ± 3.960108
Spline | 2.3153 | 0.015477 ± 0.025418
Nearest neighbour | 4.7668 | 0.008748 ± 0.003283
Natural neighbour | 1.9393 | 1.178560 ± 0.143918
Biharmonic spline | 1.5180 | 24.704136 ± 7.127264
Minimum curvature | 1.5855 | 27.111282 ± 4.487095
Shepard (p = 4) | 2.2884 | 74.327256 ± 5.358215
Kriging | 1.2249 | 91.923460 ± 13.572509

## Slide 6
Gaussian seabed: results
Original
Kriging
Nearest neighbour

## Slide 7
Gaussian seabed: results
Original
Kriging
Linear

## Slide 8
About the mission: physical bounds
AUV is supposed to move back and forth
  No steering in the inspected area
  No navigation error
Transept spacing chosen by users
  Y samples specified in the GUI
  A bound can be imposed by the AUV used (point mass in our case, no bound)
AUV velocity constraints
  No overlapping between consecutive signals
  Echosounder characteristics

## Slide 9
No signals overlapping bound
Signal must go back and forth between AUV and seabed before the next ping
: signal “travel” time
: signal duration
: AUV velocity
: samples spacing
  : area X-axis length (Seabed X in the GUI)
  : samples among X-axis (X samples in the GUI)
Travel time is maximum for the maximum detectable distance
: signal noise ratio
: detection threshold

## Slide 10
No signals overlapping bound
: received signal
: noise
: source level
: transmission loss
: target strength
Spherical spreading
: water absorption coefficient (GUI)
: distance traveled by signal

## Slide 11
No signals overlapping bound
We need to compute travel time
Using this value we can found a solution for from the transmission loss equation
: sound speed

## Slide 12
EA640 echosounder

## Slide 13
Ping rate bound
Ping rate is limited by echosounder characteristics
Ping rate can be computed as
Using previous variables
Thus

## Slide 14
Ping rate bound
From floor function definition
Thus

## Slide 15
Example
Ideal case
Notes: R = 562.3413
T_R = 0.3749 s
1 kn = 0,514 m/s

## Slide 16
Example
Possible case
Notes: Sabbia fine
Acqua a 20°C
R =61.6991 m
T_R = 0.0411 s
1 kn = 0,514 m/s

## Slide 17
Samples density
Users can change the number of samples
More samples
  Samples affected by noise
  Outliers are more likely to be present and not rejected
  Higher computational complexity
  Slower AUV
Less samples
  Less data for training
  Lower computational complexity
  Lower probability of measuring critical points
  Faster AUV (upper-bounded velocity)
Random Gaussian seabed for testing

## Slide 18
25 x 10 samples
Algorithm |  | 
Linear | 2.4736 | 0.762870 ± 0.095290
RBF | 5.3054 | 16.760720 ± 3.584874
Spline | 2.7962 | 0.008283 ± 0.001686
Nearest neighbour | 5.4114 | 0.008183 ± 0.000878
Natural neighbour | 2.4736 | 0.771853 ± 0.066545
Biharmonic spline | 2.1533 | 13.286861 ± 3.090218
Minimum curvature | 2.1615 | 12.019924 ± 1.718154
Shepard (p = 4) | 3.0798 | 52.915326 ± 4.303706
Kriging | 2.0897 | 46.071008 ± 8.019892
Algorithm |  | 
Linear | 2.4736 | 0.762870 ± 0.095290
RBF | 5.3054 | 16.760720 ± 3.584874
Spline | 2.7962 | 0.008283 ± 0.001686
Nearest neighbour | 5.4114 | 0.008183 ± 0.000878
Natural neighbour | 2.4736 | 0.771853 ± 0.066545
Biharmonic spline | 2.1533 | 13.286861 ± 3.090218
Minimum curvature | 2.1615 | 12.019924 ± 1.718154
Shepard (p = 4) | 3.0798 | 52.915326 ± 4.303706
Kriging | 2.0897 | 46.071008 ± 8.019892

## Slide 19
25 x 10 samples
Original
Kriging
Nearest neighbour

## Slide 20
50 x 10 samples
Algorithm |  | 
Linear | 1.9393 | 0.979798 ± 0.024702
RBF | 4.6236 | 37.460120 ± 3.960108
Spline | 2.3153 | 0.015477 ± 0.025418
Nearest neighbour | 4.7668 | 0.008748 ± 0.003283
Natural neighbour | 1.9393 | 1.178560 ± 0.143918
Biharmonic spline | 1.5180 | 24.704136 ± 7.127264
Minimum curvature | 1.5855 | 27.111282 ± 4.487095
Shepard (p = 4) | 2.2884 | 74.327256 ± 5.358215
Kriging | 1.2249 | 91.923460 ± 13.572509
Algorithm |  | 
Linear | 1.9393 | 0.979798 ± 0.024702
RBF | 4.6236 | 37.460120 ± 3.960108
Spline | 2.3153 | 0.015477 ± 0.025418
Nearest neighbour | 4.7668 | 0.008748 ± 0.003283
Natural neighbour | 1.9393 | 1.178560 ± 0.143918
Biharmonic spline | 1.5180 | 24.704136 ± 7.127264
Minimum curvature | 1.5855 | 27.111282 ± 4.487095
Shepard (p = 4) | 2.2884 | 74.327256 ± 5.358215
Kriging | 1.2249 | 91.923460 ± 13.572509

## Slide 21
50 x 10 samples
Original
Kriging
Nearest neighbour

## Slide 22
50 x 50 samples
Algorithm |  | 
Linear | 1.5946 | 0.864295 ± 0.053953
RBF | - | -
Spline | 2.4046 | 0.010351 ± 0.004602
Nearest neighbour | 3.2817 | 0.008439 ± 0.003877
Natural neighbour | 1.5946 | 0.862264 ± 0.053311
Biharmonic spline | 2.0046 | 104.586490 ± 7.493635
Minimum curvature | 1.9814 | 31.690825 ± 6.107661
Shepard (p = 4) | 2.0829 | 300.709037 ± 65.118698
Kriging | 1.8167 | 752.686296 ± 135.727415
Algorithm |  | 
Linear | 1.5946 | 0.864295 ± 0.053953
RBF | - | -
Spline | 2.4046 | 0.010351 ± 0.004602
Nearest neighbour | 3.2817 | 0.008439 ± 0.003877
Natural neighbour | 1.5946 | 0.862264 ± 0.053311
Biharmonic spline | 2.0046 | 104.586490 ± 7.493635
Minimum curvature | 1.9814 | 31.690825 ± 6.107661
Shepard (p = 4) | 2.0829 | 300.709037 ± 65.118698
Kriging | 1.8167 | 752.686296 ± 135.727415

## Slide 23
50 x 50 samples
Original
Natural neighbour
Nearest neighbour

## Slide 24
Nearest neighbour
250 samples
500 samples
2500 samples

## Slide 25
Kriging
250 samples
500 samples
2500 samples

## Slide 26
Linear
250 samples
500 samples
2500 samples

## Slide 27
To do
Noise filtering
Different outliers replacement
Path drawing