## Slide 1
Bathymetry interpolation algorithms using AUV mission data
Alessia Annecchini
Alessia Guida
Lorenzo Irace
Giuseppe Longo

## Slide 2
Previously on this topic
Most performant algorithms
  Ideal case: spline interpolation
  Noise: kriging and spline interpolation
  Outliers: kriging and linear interpolation
    But kriging is slow...
  Noise and outliers: linear interpolation
Performances indexes: MSE and execution time (computing 95% confidence interval on 5 repetitions)
Physical bounds
Sample density incidence

## Slide 3
Lineup
Path
Real bathymetry data
Trade-off plots

## Slide 4
Path
AUV is supposed to move back and forth
  No steering in the inspected area
  No navigation error
Samples among directions are chosen by users
  X samples
  Y samples
samples means intervals
Seabed is represented as a set of points
  Intervals have to be represented as indexes count
  In order to fully cover the area ceil function must be used

## Slide 5
Path
X samples set to 15
Y samples set to 10

## Slide 6
Path
Intervals approximation can lead to take sampling points outside the area of interest
  Cumulative error introduces an offset
There are at most points outside the are if
Where
This condition can be written as

## Slide 7
Using real data
Map
  Source: GEBCO project (www.gebco.net)
  Mirror: BODC (www.bodc.ac.uk)
  Area dimensions: approximately 100km x 100km
  Area points: 220 x 275
  Location: Mediterranean Sea
  Samples: 56 x 56
Mission
  Mission depth: 2650 m
  Noise on sampling () not filtered
  Outliers (not perfect rejection)
  Signal frequency: 10 kHz
  Signal duration: 16 ms

## Slide 8
Using real data

## Slide 9
Real seabed: results
Algorithm |  | 
Linear | 10.0 | 0.113 ± 0.102
RBF | 13.3 | 9.639 ± 0.233
Spline | 8.6 | 0.002 ± 0.001
Nearest neighbour | 47.0 | 0.001 ± 0.001
Natural neighbour | 10.0 | 0.079 ± 0.020
Biharmonic spline | 7.6 | 7.704 ± 0.560
Minimum curvature | 7.6 | 2.453 ± 0.374
Shepard (p = 4) | 19.4 | 20.982 ± 2.133
Kriging | 7.3 | 80.654 ± 13.102
Algorithm |  | 
Linear | 10.0 | 0.113 ± 0.102
RBF | 13.3 | 9.639 ± 0.233
Spline | 8.6 | 0.002 ± 0.001
Nearest neighbour | 47.0 | 0.001 ± 0.001
Natural neighbour | 10.0 | 0.079 ± 0.020
Biharmonic spline | 7.6 | 7.704 ± 0.560
Minimum curvature | 7.6 | 2.453 ± 0.374
Shepard (p = 4) | 19.4 | 20.982 ± 2.133
Kriging | 7.3 | 80.654 ± 13.102

## Slide 10
Real seabed: results
Original
Kriging
Nearest neighbour

## Slide 11
Performances trade-off
Each algorithm has its pros and cons
  Fast algorithms can have low quality results
  Good quality results can imply high computational cost
A way to visualize an appropriate trade-off is to plot performances in a Time-MSE plane
An algorithm is a point in the plane
An algorithms is better that another if it’s closer to axes origin
is the ideal algorithm: no error, no execution time
Time
MSE
Better
Best
Notes: NOTA: dire che il migliore è il più vicino all’origine vuol dire minimizzare J = MSE^2 + TIME^2 ->Hanno lo stesso peso

## Slide 12
Real seabed

## Slide 13
Real seabed
Nearest Neighbour
Kriging

## Slide 14
Real seabed: results
Original
Kriging
Minimum curvature

## Slide 15
Gaussian seabed 100m x 100m: results
Algorithm |  | 
Linear | 1.7 | 1.190 ± 0.067
RBF | - | -
Spline | 2.6 | 0.014 ± 0.003
Nearest neighbour | 3.3 | 0.010 ± 0.003
Natural neighbour | 1.7 | 1.140 ± 0.036
Biharmonic spline | 2.2 | 417.554 ± 1.786
Minimum curvature | 2.1 | 57.300 ± 2.871
Shepard (p = 4) | 2.2 | 1209.800 ± 38.591
Kriging | - | -
Algorithm |  | 
Linear | 1.7 | 1.190 ± 0.067
RBF | - | -
Spline | 2.6 | 0.014 ± 0.003
Nearest neighbour | 3.3 | 0.010 ± 0.003
Natural neighbour | 1.7 | 1.140 ± 0.036
Biharmonic spline | 2.2 | 417.554 ± 1.786
Minimum curvature | 2.1 | 57.300 ± 2.871
Shepard (p = 4) | 2.2 | 1209.800 ± 38.591
Kriging | - | -
Notes: RBF: out of memory error
Kriging: out of memory error possibile e tempo di esecuzione dell’ordine delle ore

## Slide 16
Gaussian seabed 100m x 100m: results

## Slide 17
Gaussian seabed 100m x 100m: results
Original
Linear
Minimum curvature