## Slide 1
Bathymetry interpolation algorithms using AUV mission data
Alessia Annecchini
Alessia Guida
Lorenzo Irace
Giuseppe Longo

## Slide 2
Project overview
Project goal: analysis of interpolation algorithms to reconstruct bathymetry from mission data
  Echosounder single-beam (EA670 from Kongsberg Marine used as reference)
Software goal: Matlab GUI able to collect parameters set by user, to simulate mission and to apply interpolation algorithms

## Slide 3
Project steps
Problem modeling
Algorithms
Performances evaluation
Conclusions

## Slide 4
Problem modeling
Seabed shapes
  Plane
  Step
  Product of sinusoids
  Filtered Gaussian process
  Data from external source
    GEBCO: Mediterranean seabed
    Other project: inclined plane and irregular path
Acoustic signal modeling
  Monostatic active sonar
  Perfectly vertical
  Water absorption ()
  Seabed composition ()
  Average ambient noise ()
Problem modeling
Algorithms
Performances evaluation
Conclusions

## Slide 5
Problem modeling
Noise
  White Gaussian
  Small, not filtered
Outliers
  Higher magnitude than noise
  Randomly generated
  Not perfectly rejected
Path
  AUV considered as a point mass
  Moving back and forth
  No navigation error
  No steering in the inspected area
  Velocity constraints
    No overlapping between consecutive signals
    Ping rate bounded
Problem modeling
Algorithms
Performances evaluation
Conclusions

## Slide 6
Problem modeling
Samples density
  Seabed represented as a matrix
  Spaces between samples approximation
  Constraint on the number of samples
Before data can go through algorithms we have…
Problem modeling
Algorithms
Performances evaluation
Conclusions
Seabed generation
Mission simulation
Samples elaboration
Samples as signal power collected by sensor
Power to distance
Outliers rejection
Seabed matrix

## Slide 7
Algorithms
Can require gridded or scattered data
Different computational cost
Different spatial subdivision
Different guaranteed continuity
Global or only local (irregular path)
Problem modeling
Algorithms
Performances evaluation
Conclusions
Algorithm | Only grid | Continuity | Additional information | Global/local
Linear | No |  | - | Local
RBF | No |  | Neural Network | -
Spline | Yes |  | - | -
Nearest neighbor | No | Discontinue | No new data | Local
Natural neighbor | No |  | - | Local
Biharmonic spline | No |  | - | Global
Minimum curvature | No |  | - | Global
Shepard | No |  | Additional parameter p | Global
Kriging | Yes |  | Min MSE on samples | -
Algorithm | Only grid | Continuity | Additional information | Global/local
Linear | No |  | - | Local
RBF | No |  | Neural Network | -
Spline | Yes |  | - | -
Nearest neighbor | No | Discontinue | No new data | Local
Natural neighbor | No |  | - | Local
Biharmonic spline | No |  | - | Global
Minimum curvature | No |  | - | Global
Shepard | No |  | Additional parameter p | Global
Kriging | Yes |  | Min MSE on samples | -

## Slide 8
Algorithms
Problem modeling
Algorithms
Performances evaluation
Conclusions
Seabed
Mission
Depth samples
X-grid
Y-grid
Z-grid
(X, Y)
Z
Gridded data
h
k
h
k
h
k
h
k
k*h
k*h
2
1
Scattered data
Algorithm
Comparison
Interpolated seabed
a
a
b
b
k < a, h < b

## Slide 9
Performances evaluation
Quality indexes
  Mean Square Error ()
  Execution time
Trade-off graphically represented by Time-MSE graphs
Tests in different conditions and for different shapes
  Ideal
  Only noise
  Only outliers
  Noise and outliers
  Samples density variation
  External data
Problem modeling
Algorithms
Performances evaluation
Conclusions
Time
MSE
Better
Best

## Slide 10
Conclusions
No algorithm is comprehensively better than others
The algorithm must be chosen based on problem features
Real-time application
  Linear interpolation
  Natural neighbour interpolation
  Spline interpolation
High quality results
  Kriging interpolation
  Minimum curvature interpolation
Interpolation quality is bounded by the presence of noise and outliers
Problem modeling
Algorithms
Performances evaluation
Conclusions

## Slide 11
Conclusions
Increasing the number of samples does not always imply higher quality due to imperfections
Problem modeling
Algorithms
Performances evaluation
Conclusions

## Slide 12
Conclusions
If data do not cover the entire area a global interpolation seems more suitable than a local one, but good results are not always guaranteed
Problem modeling
Algorithms
Performances evaluation
Conclusions
Natural neighbour interpolation
Minimum curvature interpolation
Shepard interpolation

## Slide 13
Thank you
for the attention!